## Slide 1: LAR TO GAR AND TRACK RECONSTRUCTION: FUTURE PLANS AND CURRENT STATUS
Presents: Federico Battisti

## Slide 2: Lar to Gar sample: motivation and current procedure
An important role of ND-GAr will be to function as a muon spectrometer of ND-LAr: to evaluate its capabilities in that sense the propagation of tracks needs to be very well studied
The current ND simulation chain:
  Simulate neutrino interactions with GENIE in a ND hall geometry file containing only the liquid Argon detector
  Propagate particles using edep-sim in a ND hall geometry file containing both ArgonCube and HPgTPC
  Convert edep-sim file to root file readable by GarSoft
  Follow the Garsoft reconstruction chain
Recently a wiki has been developed by Eldwan Brianne : https://cdcvs.fnal.gov/redmine/projects/dune-neardet-design/wiki/Run_edep-sim_samples_through_GArSoft

## Slide 3: Lar to gar sample: an example
Two examples of interactions in ArgonCube one with a passing muon reaching NDGAr, the other without (both made with edep-disp)
PASSING MUON
NON-PASSING MUON

## Slide 4: Lar to gar sample: improvements
Strong need for large LAr samples already propagated in edep-sim to test the chain
L2G: interface that takes outgoing LAr particles and feeds them to edep-sim with any TMS detector could speed up the sample production (Currently starting to work on it with Eldwan towards TMS meeting)
Constant B-field currently being used (Custom B-field is already implemented in edep-sim/GArSoft )
Need to improve the track reconstruction and fitting
https://indico.fnal.gov/event/44562/contributions/200915/attachments/136745/170170/DUNE_ND_Meeting_28.10.20.pdf

## Slide 5: Track finding and fitting in gar
Track finding:
  Find hits (i.e. pulses found on a single channel)
  Group nearby hits in space and time and find their charge centroids found: TPC Clusters
  Find track segments (vector hits) and associate them with TPC Clusters
  Cluster vector hits together into track candidates
y
z
x
Track fitting: Kalman filter is applied to the track candidates two times in order to compute the best estimates of the track parameters on both ends of the track (Developed by Thomas Junk and Leo Bellantoni: https://docs.dunescience.org/cgi-bin/private/ShowDocument?docid=13933)

## Slide 6: KALMAN FILTER
A Kalman filter is an iterative algorithm which uses a system's physical laws of motion, known control inputs and multiple sequential measurements to form an estimate of the system's varying quantities
At each step of the iteration an estimate of the state of the system is produced as a weighted average of the system's predicted state and of the new measurement. The weights are calculated from the covariance.
The extended Kalman filter expands the Kalman filter technique to non-linear systems
The models for state transition and measurement can be written as:
Where is the function of the previous state, , and the control input, , that provides the current state . is the measurement function that relates the current state, , to the measurement . and are Gaussian noises for the process model and the measurement model with covariance 𝑄 and 𝑅, respectively

## Slide 7: EXTENDED KALMAN FILTER ALGORITHM
Make a priori predictions for the current step’s state and covariance matrix using the a posteriori best estimate of the previous step (i.e. updated using measurement)
JACOBIAN
CONVERSION MATRIX
PROCESS NOISE COVARIANCE
STATE VECTOR
COVARIANCE MATRIX
Note: In the first iteration step we use step 0 estimates for the state vector and the covariance matrix (), which can be made very roughly

## Slide 8: EXTENDED KALMAN FILTER ALGORITHM
Calculate the measurement residual and the Kalman Gain
Update the estimate
RESIDUAL
KALMAN GAIN
STATE VECTOR
COVARIANCE MATRIX
MEASUREMENT NOISE COVARIANCE

## Slide 9: KALMAN FILTER APPLICATION
We want to apply the extended Kalman filter to the motion of a charged particle in the magnetic field
TRACK PARAMETERS
We apply the Kalman filter to track candidates, consisting of groups of TPC clusters, which are identified and put together during the reconstruction process. Each step of the Kalman filter algorithm is identified by one of these TPC clusters
T. Junk, DUNE-Doc-13933
https://docs.dunescience.org/cgi-bin/private/ShowDocument?docid=13933

## Slide 10: KALMAN FILTER APPLICATION: initial estimates
Before the Kalman filter algorithm can be applied, we need an initial estimate for the state vector, which in our case includes and the covariance matrix
STATE VECTOR
COVARIANCE MATRIX
The estimated quantities from the state vector can be used to estimate the particle’s momentum

## Slide 11: KALMAN FILTER APPLICATION: prediction AND MEASUREMENT
From the equation of motion we obtain the prediction function for our state vector.
The only measured quantities in our case are and , and are set at the center of the TPC cluster correspondent to the present step.
Note: the prediction model does not account for dE/dx energy loss

## Slide 12: KALMAN FILTER APPLICATION: STEP DEtermination
Each algorithm step corresponds to a TPC cluster. The x coordinate is treated as independent and used to identify the step width . The step width is determined for each algorithm step, so that it minimizes:
and are the errors associated with the TPC Clusters
For each step we then have:
Note: despite being our free parameter, x is associated with an uncertainty; other options might be worth exploring

## Slide 13: KALMAN FILTER APPLICATION: COVARIANCE MATRIX PREDICTION
First step to make the prediction for the covariance matrix is to calculate the Jacobian
The step uncertainty matrix is also needed
The prediction is then:

## Slide 14: KALMAN FILTER APPLICATION: Evaluate the residual
We now evaluate the residual and Kalman Gain
KALMAN GAIN
RESIDUAL
With:
CONVERSION MATRIX
MEASUREMENT NOISE COVARIANCE
Note: The uncertainties in R are fixed, before the Kalman filter is applied, as external parameters: R is not updated.

## Slide 15: KALMAN FILTER APPLICATION: PREDICTION UPDATE
We are now finally able to update our estimates using both the a priori prediction and the measurement
STATE VECTOR
COVARIANCE MATRIX

## Slide 16: KALMAN FILTER APPLICATION:
The Kalman filter algorithm is applied to the track candidate both ways (i.e. From first TPC cluster to last and vice versa) and each time a value is calculated
Where is the residual typical value which depends on the particle trajectory position in the detector and the tracking planes (fixed values evaluated a priori)

## Slide 17: KALMAN FILTER: PERFORMANCE evaluation
Plots describing the evolution of the estimate for the measured quantities as a function of the free parameter (Information retrieved directly modifying the kalman filter module in garsoft tpctrackfit2_module.cc) for a muon from a particle gun pointing towards the center of the TPC. FORWARD FIT
Note: the energy loss (dE/dx) of the particle along the track causes the particle to slow down and the track parameters (i.e the curvature) to change. The Kalman filter updates step by step its estimates using measurement and taking into account these changes: for this reason the Forward and Backward fits will produce different results, despite being performed with the same procedure
FITTER PROPAGATION DIRECTION

## Slide 18: KALMAN FILTER: PERFORMANCE evaluation
Plots describing the evolution of the estimate of the measured quantities as a function of the free parameter (Information retrieved directly modifying the kalman filter module in garsoft tpctrackfit2_module.cc) for a muon from a particle gun pointing towards the center of the TPC: BACKWARD FIT
FITTER PROPAGATION DIRECTION
Note: at the moment the Kalman gain is calibrated in such a way to strongly favour the a priori prediction over the measurement; this might not be the ideal choice

## Slide 19: KALMAN FILTER PERFORMANCE
Plots describing the evolution of the estimate of the non measured quantities as a function of the free parameter : FORWARD FIT
FITTER PROPAGATION DIRECTION
19

## Slide 20: KALMAN FILTER PERFORMANCE
Plots describing the evolution of the estimate of the non measured quantities as a function of the free parameter BACKWARD FIT
FITTER PROPAGATION DITECTION
20

## Slide 21: KALMAN FILTER PERFORMANCE
Plots comparing the best estimate from the Kalman fitter algorithm for the measured quantities as a function of the free parameter with the MC Truth values: FORWARD FIT
FITTER PROPAGATION DIRECTION

## Slide 22: KALMAN FILTER PERFORMANCE
Plots comparing the best estimate from the Kalman fitter algorithm for the measured quantities as a function of the free parameter with the MC Truth values: BACKWARD FIT
FITTER PROPAGATION DIRECTION

## Slide 23: KALMAN FILTER PERFORMANCE
Plots comparing the reconstructed tansverse momentum from the Kalman fitter algorithm to the MC truth as a function of the free parameter
FORWARD FIT
BACKWARD FIT

## Slide 24: KALMAN FILTER PERFORMANCE
Plots comparing the reconstructed total momentum p from the Kalman fitter algorithm to the MC truth as a function of the free parameter
FORWARD FIT
BACKWARD FIT

## Slide 25: SUMMARY AND FUTURE STEPS
The simulation chain is up and running, but much larger samples are needed
  L2G: interface that takes outgoing LAr particles and feeds them to edep-sim with any TMS detector (currently starting to develop with Eldwan)
In the Kalman Filter algorithm, at the moment, dE/dx (which is simulated in the MC propagation) is not taken into account in the prediction step and only accounted for by a posteriori measurement corrections
  dE/dx inclusion in the prediction step could alleviate biases in the reconstruction
Optimize the choice for the free parameter (currently drift coordinate) in the Kalman filter procedure
Optimize the Kalman gain so that the measurements have more weight in the prediction
In the context Kalman filter and reconstruction in general need to be expanded to project tracks backwards to NDLAr and connect with the liquid Argon reconstruction information

## Slide 26: KALMAN FILTER PERFORMANCE
Applied Kalman Filter to ideal measurements following perfectly an helix with initial coordinates: and the free parameter and the step

## Slide 27: KALMAN FILTER PERFORMANCE
Plots describing the evolution of the estimate of the measured quantities as a function of the free parameter for the perfect helix. Note that the the fake TPC points have on the x coordinate the fake measured value, while for the estimates we use the estimated x (i.e. )
FITTER PROPAGATION DIRECTION

## Slide 28: KALMAN FILTER PERFORMANCE
Plots describing the evolution of the estimate of the measured quantities as a function of the free parameter for the perfect helix. This time both the fake TPC points have on the x coordinate the fake measured value
FITTER PROPAGATION DIRECTION

## Slide 29: KALMAN FILTER: PERFORMANCE evaluation
Going back to the anomalous backward fit plots, we first plot them like it was done originally (i.e. the fake TPC points have on the x coordinate the fake measured value, while for the estimates we use the estimated x )
FITTER PROPAGATION DIRECTION

## Slide 30: KALMAN FILTER: PERFORMANCE evaluation
We now try using the measured value of x for everything
FITTER PROPAGATION DIRECTION